## Slide 1: Thermal analysis & Tests UPMSat-3
De Ávila Cabral, Sergio
22/04/2024

## Slide 2: Table of content
Introduction & Objectives
GMM & TMM
Instruments temperatures
Thermal Hardware
Conclusions

## Slide 3: 1. Introduction & Objectives
UPMSat-3 Mission
Thermal Analysis
Operational Requirements
Survival Requirements
Thermal Hardware Design
Thermal vacuum testing
Figure 1: ESTAN-TMS model.
Notes: Dentro de marco de la mission UPMSat

## Slide 4: 2. GMM & TMM
Figure 2: Materials applied in the model.
Notes: Str + SP => Modelado más detallado.

## Slide 5: 2. GMM & TMM: Thermo-optical properties
Silvered FEP
Kapton + CFRP
Solar cell.
PCB
Surtec 650
DELRIN
Black Anodize
Aluminium
Aluminised Kapton
Figure 3: Thermo-optical properties applied in the model.
CFRP
Notes: Absortividad corregida de las células solares.

## Slide 6: 2. GMM & TMM: Materials
Solar Panels eq1.
GaAsGe
PCB eq1.
DELRIN
Al-7075-T651
Al-6082
Al-6061
Figure 4: Materials applied in the model.
1: Equivalent properties.

## Slide 7: 2. GMM & TMM: Analysis Cases
Analysis case | Radiative Case | Dissipation [W]
Latency Cold | Cold | 1.00
Latency | Standard | 1.00
Nominal | Standard | 7.65
PL1 Cold | Cold | 15.65
PL1 | Standard | 
PL1 Hot | Hot | 
PL2 | Standard | 9.65
Safe | Standard | 7.65
 | Cold | Standard | Hot
Albedo coeff. | 0.226 | 0.306 | 0.336
[K] | 249.0 | 254.3 | 260.0
 | Cold | Standard | Hot
Albedo coeff. | 0.226 | 0.306 | 0.336
 | 249.0 | 254.3 | 260.0
Table 1: STEM results.
Table 2: Analysis cases.

## Slide 8: 3. Instruments temperatures
to 60C
𝑇_𝑜𝑝𝑠=[−10 °"C" to 60°C]
to 7C
𝑇_𝑠𝑢𝑣=[−10 °"C" to 70°C]
C
𝑇_𝑏𝑎𝑡>10 °C
Temperature ranges
Latency Cold: Instruments
Latency Cold: Payload
PL1: Instruments
PL1: Payload
Figure 7: Instruments temperature in PL1.
Figure 5: Instruments temperature in Latency Cold.
Figure 6: Payload temperature in Latency Cold.
Figure 8: Payload temperature in PL1.

## Slide 9: 4. Thermal Hardware: Radiator
Radiator
Dim: 100 x 130 mm
Mat: Al-6061
Front: Silvered FEP
Back: Alum. Kapton
Frame
Mat: DELRIN
Eight contact points
Dim: 121.2 x 151.2 mm
Figure 9: Radiator 3D model.

## Slide 10: 4. Thermal Hardware: Radiator
Figure 10: Radiator Absorbed Heat flow.
Figure 11: Heat flow between Frame - LP and Frame - Radiator.
Figure 12: Heat Flow between BF- Radiator.
Figure 13: BF temperatures.

## Slide 11: 5. PCB-UC3M Test
Passive PCB Dim: 68.6 x 30.0 x 0.8 mm
Temperature range
C
𝑇_𝑚𝑎𝑥=50 °C
C
𝑇_𝑚𝑖𝑛=−40 °C
Allowed tolerance : C
Allowed tolerance : 𝑇_𝑒𝑟𝑟𝑜𝑟=±3 °C
Stay time: 30 min
Minimum cycles: 8
Passive PCB Dim: 68.6 x 30.0 x 0.8 mm
Temperature range
Stay time: 30 min
Minimum cycles: 8
Figure 12: PCB-UC3M 3D model.
Figure 13: Setup
Thermal test.

## Slide 12: 5. PCB-UC3M Test
Total time: approx. 26 hours.
Time per cycle: 2.5 hours approx.
Passive PCB Dim: 68.6 x 30.0 x 0.8 mm
Temperature range
C
𝑇_𝑚𝑎𝑥=50 °C
C
𝑇_𝑚𝑖𝑛=−40 °C
Allowed tolerance : C
Allowed tolerance : 𝑇_𝑒𝑟𝑟𝑜𝑟=±3 °C
Stay time: 30 min
Minimum cycles: 8
Passive PCB Dim: 68.6 x 30.0 x 0.8 mm
Temperature range
Stay time: 30 min
Minimum cycles: 8
Figure 14: Thermal test results.

## Slide 13: 6. Conclusions
Survival and operating requirements are met in all modes of operation.
Thermal Hardware required:
  Insulating supports.
  Radiator and frame.
  Active Thermal Control.
Radiator sized for non-optimum conditions.
Need of model refinement to obtain more accurate data and reduce the level of uncertainty.
Perform thermal vacuum test.

## Slide 14: Thanks for your attention Questions?

## Slide 15
Referencias
[1] | Et al. Ignacio Torralbo. «Thermal Analysis of the Solar Orbiter PHI Electronics Unit». En: (2020).
[2] | David G. Gilmore. Spacecraft Thermal Control Handbook. The Aerospace Press, 2002. isbn: 1-884989-11-X.
[3] | Sergio De Ávila Ahmad Khalaf. Test Report / Test Result. Thermo-Optical Properties of Surtec 650. Instituto de Migrogravedad Ignacio Da Riva (IDR), 2023.
[4] | Mechanical and Electrical ICD Radiometer Payload. Inf. téc. Universidad Carlos III de Madrid, 2023.

## Slide 16
Referencias
[5] | Et al. Ignacio Torralbo. «Thermal Analysis of the Solar Orbiter PHI Electronics Unit». En: (2020).
[6] | AzurSpace: 30% Triple Junction GaAs Solar Cell Type: TJ Solar Cell 3G30C Advanced.
[7] | EESEM. Properties of Si, Ge, and GaAs at 300K. url: eesemi.com/sigegaas.htm.
[8] | ASM Aerospace Specificacions Metas Inc. MatWeb. url: https://www.matweb.com/

## Slide 17: Model evolution

## Slide 18: Model evolution

## Slide 19: Model evolution